## Slide 1
Nordic CCC
Martin Julander
2019-10-08

## Slide 2
A layer between operations & energy market..
Capacity Calculation
System Operator
Market Operator
Exchange Capacity
Power System

## Slide 3: Why capacity restrictions?
The electrical grid has a limited capacity for transporting power
Try transferring too much power, and the system is at risk of collapse
Capacity restrictions are necessary to ensure stable electricity supply with high quality
Capacity restrictions are only one of the tools employed by the TSOs to ensure operational security

## Slide 4
Capacity calculation is the process of translating the complex physical grid into a simplified form that can be understood and applied by the power exchange
Complexity
Simplicity
FB
CNTC
Detailed grid model
The physical world
The commercial world
Capacity Calculation
System Operator

## Slide 5
Capacity allocation is the process of maximizing social welfare, whilst respecting the physical constraints of the power system
Optimization
Capacities (constraints)
Capacity Allocation
Bids
Buy
Sell
Prices, Net Positions => Scheduled flows
Market Operator

## Slide 6: Transit flows of one bilateral exchange
0.7 %
0.7 %
24 %
24 %
0 %
0.7 %
20 %
8 %
56 %
24 %
12 %
0.1 %
0.1 %
12 %
FB
Commercial Exchange
Commercial Flow (NTC)
Flow factor
Trade
Flow factor (PTDF)

## Slide 7: Capacity calculation – (C)NTC
Capacity is provided as MW limits on exchange on each BZ border
The market does not know real physics, and capacities are perceived as simultaneously available
A
C
B
Max injection of 2000 MW
Max Extraction of 2000 MW
1000 MW
1000 MW
Physical capacity
1000 MW
667 MW
Physical flow
667 MW
1333 MW
Overload
Cannot provide the physical capacity on all lines at the same time because it allows for physical overloads
Exchange Capacities must be reduced
in order to maintain operational security
A
C
B
Max injection of 1500 MW
Max Extraction of 1500 MW
750 MW
750 MW
Exchange capacity
750 MW
500 MW
Physical flow
500 MW
1000 MW
Unutilized capacity
Not OK
OK
Exchange capacity
=
Market constraint: NP ≤ j CNTCj

## Slide 8
Flow based – PTDF, CNE & Fmax
A
C
B
PTDFA = 33%
PTDFA = 33%
PTDFA = 67%
Capacity is provided by PTDFs, and CNEs with a MW limit/margin
The market knows a linearized version of the real physics and understands that capacities are interdependent
The lines (a-b), (b-c) and (a-c) are CNEs
The physical capacity for each line is provided (Fmax = 1000 MW)
The PTDFs shown are the flows induced on each line by a net injection in A and extracted in C (slack node), each BZ will have a unique PTDF on each CNE
The FB capacities constitute a simplified grid model to be applied by the power exchange
67 MW
100 MW
100 MW
33 MW
33 MW
Fmax = 1000 MW
Fmax = 1000 MW
Fmax = 1000 MW

## Slide 9: How bilateral exchanges are perceived by the market algorithm in FB and CNTC
CNTC
FB

## Slide 10
Nordic Capacity Calculation - Today
NTC
NTC
NTC
NTC

## Slide 11
Coordinated Capacity Calculator (CCC)
CCC
FB / CNTC
Input to capacity calculations
Nordic Metodologies
Day-Ahead Capacities: Flow Based
Intraday Capacities: Flow Based
(CNTC as interim until XBID supports Flow Based)
Long-term Capacities: ACER decision

## Slide 12
.. and Multiple NEMOs
CCC
FB / CNTC
Input to capacity calculations
?

## Slide 13
Backup slides

## Slide 14
Physical limitations and exchange capacity

## Slide 15
Flow Based
Complexity
Simplicity
FB
CNTC
Detailed grid model
CNTC and FB describes physical transfer limitations of the power system
CNTC and FB are used as constraints in market allocation (exchange capacity)
FB describes the constraints in higher detail, which enables better optimization (larger domain)

## Slide 16
Physical capacity
The physical capacity is defined by the components of the power-grid and the state of the power system
Due to operational security and risk considerations, the secure physical capacity applied in operation will/may differ from the maximum found in any given scenario
Thus, the secure physical capacities of grid components will vary with grid topology, temperatures, loading and risk assessment
The secure physical capacity is a common base for the FB and CNTC capacity calculation
The physical capacities constitute complex non-linear limitations on flows
  Thermal limitations for each grid element
  Steady state and dynamic voltage limits for each grid element or group of elements
  Dynamic stability limits for groups of grid elements
  Short circuit limits
  N-1 considerations
Complexity
Simplicity
FB
CNTC
Detailed grid model

## Slide 17
Exchange capacity
Exchange capacity is derived from the secure physical capacity to provide MW limits for commercial power exchanges
Exchange capacity provides limitations for the electricity market, in terms of linearized constraints, on cross zonal exchanges. The linearized constraints are simplifications of the complex non-linear secure physical limitations of the grid
There are two options for providing exchange capacity for the electricity market:
  FB: The electricity market receives a linearized security domain described by power transfer distribution factors (PTDFs) on critical network elements (CNEs). The flow on each individual CNE is limited by a MW margin representing the secure physical capacity of the component(s), while the PTDF gives the flow on each CNE from a one MW injection in each BZ
  CNTC: The electricity market receives a MW limit on bilateral exchanges between bidding zones. The MW limits are derived from the security domain where bidding zone configuration is applied in order to capture all relevant limitations
Complexity
Simplicity
FB
CNTC
Detailed grid model

## Slide 18: How bilateral exchanges are perceived by the market algorithm in FB and CNTC
CNTC
FB

## Slide 19: Capacity calculation - Example
Simplifying assumptions
No internal CNEs/grid constraints
Only one node in each bidding zone
The only CNEs are the tie lines
No reliability margin
No contingencies
No remedial actions
A
C
B
Fmax = 1000 MW
Fmax = 1000 MW
Fmax = 1000 MW
Example
A power grid consisting of 3 bidding zones and three identical lines with the physical capacity of 1000 MW each – having equal impedances

## Slide 20: Capacity calculation – (C)NTC
Capacity is provided as MW limits on exchange on each BZ border
The market does not know real physics, and capacities are perceived as simultaneously available
A
C
B
Max injection of 2000 MW
Max Extraction of 2000 MW
1000 MW
1000 MW
Physical capacity
1000 MW
667 MW
Physical flow
667 MW
1333 MW
Overload
Cannot provide the physical capacity on all lines at the same time because it allows for physical overloads
Exchange Capacities must be reduced
in order to maintain operational security
A
C
B
Max injection of 1500 MW
Max Extraction of 1500 MW
750 MW
750 MW
Exchange capacity
750 MW
500 MW
Physical flow
500 MW
1000 MW
Unutilized capacity
Not OK
OK
Exchange capacity
=
Market constraint: NP ≤ j CNTCj

## Slide 21
(C)NTC – Net Transfer Capacity
Capacity is provided as MW limits on exchange on each BZ border
The full set of CNTC values are referred to as a CNTC domain, there is an unlimited set of potential CNTC domains available
Complicated to manage in highly meshed grids with many BZs
Flow determination is not a part of the market coupling (comes after), and thus there might be large differences between scheduled and physical flows
A
C
B
NTC = 750 MW
NTC = 750 MW
NTC = 750 MW
Fmax = 1000 MW
Fmax = 1000 MW
Fmax = 1000 MW

## Slide 22
Flow based – PTDF, CNE & Fmax
A
C
B
PTDFA = 33%
PTDFA = 33%
PTDFA = 67%
Capacity is provided by PTDFs, and CNEs with a MW limit/margin
The market knows a linearized version of the real physics and understands that capacities are interdependent
The lines (a-b), (b-c) and (a-c) are CNEs
The physical capacity for each line is provided (Fmax = 1000 MW)
The PTDFs shown are the flows induced on each line by a net injection in A and extracted in C (slack node), each BZ will have a unique PTDF on each CNE
The FB capacities constitute a simplified grid model to be applied by the power exchange
67 MW
100 MW
100 MW
33 MW
33 MW
Fmax = 1000 MW
Fmax = 1000 MW
Fmax = 1000 MW

## Slide 23: Flow Based Domain
The "full" security domain is provided directly as capacity to the market in the form of PTDFs and CNEs with MW margins
The security domain is uniquely defined by the grid model
Line (CNE) | Max flow (Fmax) | PTDFs for BZ A | PTDFs for BZ B | PTDFs for BZ C (slack)
A -> B (CNE 1) | 1000 MW | 33 % | - 33 % | 0
B -> C (CNE 2) | 1000 MW | 33 % | 67 % | 0
A -> C (CNE 3) | 1000 MW | 67 % | 33 % | 0
The PTDFs are calculated by the CGM and thus depend on the impedances in the grid
In this setting, the security domain is often referred to as the FB domain
Features of FB
Allows for price differences between uncongested areas - increases the ability of the market to utilize all available capacity
The market coupling solves both net positions and flows and thus scheduled and physical flows are converging
The FB domain is uniquely defined
FB capacities
A
C
B

## Slide 24: FB vs CNTC
A
C
B
750
750
750
A
C
B
1000
1000
NTC (1)
FB
1000
PTDFs
PTDFs
PTDFs
A
C
B
1000
1000
0
NTC (2)
Max import/export in all BZs are 1500 MW
Max import/export in C is 2000 MW
Max import/export in A and B is 1000 MW
Max import/export in all BZs are 2000 MW (but not all at the same time)

## Slide 25: It gets slightly more complicated in the real world,……..
12 BZs in the Nordics + 14 more virtual BZ to manage the HVDCs
70-90 limiting CNEs monitored in both directions for every hour
Both internal and cross-zonal CNEs
Bidding Zones are not copper plates – net positions distribute within a BZ, why Generation Shift Keys are needed
Application of remedial actions, contingencies and reliability margins for all CNEs