## Slide 1
MARI
Manually Activated Reserves Initiative
BSG Meeting
5 March 2018
Brussels, Belgium

## Slide 2
MARI Members Update

## Slide 3
Involved Parties – TSOs only
MEMBERS (25 TSOs) |  |  | 
Austria |  | Latvia | 
Belgium |  | Lithuania | 
Czech Republic |  | Norway | 
Denmark |  | Netherlands | 
Estonia |  | Portugal | 
Finland |  | Poland | 
France |  | Romania | 
Germany |  | Slovenia | 
 |  | Spain | 
 |  | Sweden | 
 |  | Switzerland | 
Greece |  | United Kingdom | 
Italy |  |  | 
OBSERVERS (3 TSOs + ENTSO-E) | 
Bulgaria | 
Serbia | 
Slovakia | 
Entso-E | 
TSOs in Process of Becoming Members | 
Hungary | 
Croatia | 

## Slide 4
mFRR and aFRR Platform Submission Timeline

## Slide 5
PICASSO and MARI Timeline for IFs Submission
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Stakeholder Workshops
TSOs
Stakeholders
IF Provision to NRAs
TSOs
Public Consultation – 2 Months
Implementation Framework Drafting
TSOs
Finalization on the Implementation Framework
Stakeholder Workshop

## Slide 6
Feedback from the Consultation

## Slide 7
General Statistics I
Chart: 
| Austria | Belgium | Czech Republic | Denmark | EU | Finland | France | Germany | Great Britain | Italy | Lithuania | Netherland | Norway | Slovakia | Slovenia | Spain | Sweden | Switzerland
 | 12 | 3 | 2 | 4 | 4 | 2 | 5 | 12 | 1 | 2 | 1 | 1 | 6 | 1 | 1 | 3 | 3 | 2
There were released consultation questionnaire including 45 questions, across 65 stakeholders from 17 countries.
The market roles of stakeholders were identified by themselves to 7 categories.
Majority of stakeholders is presented in Germany and Austria, and major role is the generation.
Chart: 
| Austria | Belgium | Czech Republic | Denmark | EU | Finland | France | Germany | Great Britain | Italy | Lithuania | Netherland | Norway | Slovakia | Slovenia | Spain | Sweden | Switzerland
Generation | 7 | 1 | 2 | 2 | 2 | 3 | 6 | 2 | 1 | 5 | 1 | 1 | 2.5 | 2 | 0.5
Portfolio Manager | 1 | 1 | 1 | 2 | 1
Supply | 2 | 2 | 0.5 | 0.5
Consultancy | 2
Aggregator | 2 | 1
Association | 1 | 4 | 2 | 1 | 1 | 1
Market Operator | 1
Chart: 
| Generation | Portfolio Manager | Supply | Consultancy | Aggregator | Association | Market Operator
Austria | 7 | 1 | 2 | 2
Belgium | 1 | 2
Czech Republic | 2
Denmark | 2 | 1 | 1
EU | 4
Finland | 2
France | 3 | 1 | 1
Germany | 6 | 2 | 2 | 2
Great Britain | 1
Italy | 2
Lithuania | 1
Netherland | 1

## Slide 8
General Statistics II
Chart: 
| Generation | Portfolio Manager | Supply | Consultancy | Aggregator | Association | Market Operator
 | 38 | 6 | 5 | 2 | 3 | 10 | 1
There were identified 3 size categories by mFRR capacity available:
  small (less than 5 MW)
  medium (5-100 MW)
  large (over 100 MW)
  25 stakeholders did not provide information
Chart: 
| Small | Medium | Large | Not Answered
 | 2 | 12 | 26 | 25
 | 0.030769 | 0.18462 | 0.4 | 0.38462
Chart: 
| Austria | Belgium | Czech Republic | Denmark | EU | Finland | France | Germany | Great Britain | Italy | Lithuania | Netherlands | Norway | Slovakia | Slovenia | Spain | Sweden | Switzerland
Small | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
Medium | 7 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 0
Large | 3 | 1 | 1 | 2 | 0 | 2 | 1 | 5 | 0 | 0 | 1 | 0 | 5 | 1 | 0 | 2 | 0 | 2
Not Answered | 2 | 2 | 0 | 1 | 4 | 0 | 3 | 7 | 0 | 2 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0

## Slide 9
Feedback from the Consultation
PRODUCT and PROCESS

## Slide 10
Feedback Product and Process – Main Input
A FAT of 12,5’ (or lower) would reduce the volume BSPs could offer from thermal units (-10 to -40%), which can have impact on liquidity.
FAT
Current Consideration in the Project
The Project currently favours to set the FAT as long as possible most likely at 12,5 minutes since as we “consolidate” the reserves through Europe to get benefits of the cooperation. This sets new requirements on the processing time linked to this cooperation: thus the platform will probably need 2.5’ for this purpose

## Slide 11
Feedback Product and Process – Main Input
Opportunity for the BSPs to have a limitation on number of QHs activated and the use of a “resting time” is considered to be useful for increasing participation from certain technologies (e.g. Storage, hydro and less flexible plants);
Resting Time
The feedback was not conclusive, since different preference on questions connected with the sequence were provided by the same stakeholders
It seems that BSPs prefer DA before SA based on the argument that most of the energy is delivered in the main QH.
Sequence – DA>SA vs.
SA>DA
BSP GCT should be defined on a cross project level
BSP GCT

## Slide 12
Feedback Product and Process – Main Input
A large portion of the BSPs welcome the feature of linked bids as long as there is not a massive impact on the complexity.
BSPs asked for the possibility for the to link bids between two QHs for:
start-up reasons (BPS starts-up in QH 0 hence price of the bid in QH 1 is lower)
power plant technical reasons (need for a minimum delivery period >5’)
BSPs requested more detailed information and transparency on how linking between bids is performed.
Linking Bids
Current Consideration in the Project
The feature of the linking bids shall be implemented. For the start up costs – possibility of technical linking will be further evaluated.
Optimization for technical reason will most likely not be possible – mFRR platform will most likely not allow linking over a number of QHs

## Slide 13
Feedback Product and Process – Main Input
For granularity of bids a good compromise between liquidity and efficiency/costs for implementation, would be 1 MW. BSPs foresee to use indivisible bids. In a portfolio based approach there is no need for indivisible bids but if needed, the maximum volume of indivisible bid should not be too high in order to incentivize flexibility for BSPs.
BSPs request the possibility to declare a minimum activation for technical reasons in divisible bids
Indivisibility of Bids
Current Consideration in the Project
The TSOs favour no limit on indivisible bids in order not exclude any current participants from the mFRR market

## Slide 14
Feedback Product and Process – Main Input
BSPs asked for no limitations on the volume activated by a TSO as long as there is capacity and ATC available. Proposal would be to develop the “guaranteed volume” + “excess volume” approach.
Activation Volume

## Slide 15
Feedback from the Consultation
SPECIFICATION of the ALGORITHM OPTIMAZATION FUNCTION

## Slide 16
Feedback Specification of the AOF - Main Input
Publication of inputs (TSO Demand, price, ATC per border) and outputs (submitted and activated bids and marginal prices, upward and downward volumes per bidding zone and used cross-zonal capacity) are important
Algorithm Inputs and Outputs
Social welfare maximization as objective and requirement for traceable and transparent algorithm results
Social Welfare Maximisation
Part of the responses favour scheduled counteractivations inter-alia because increases the probability for BSPs to be activation. Other BSPs stake that TSO should use flexibility when they need it for system security, not for market issues.
Scheduled counter-activations

## Slide 17
Feedback Specification of the AOF - Main Input
The BSPs are in general against unforeseeably accepted divisible bids however could accept unforeseeable rejected divisible bids for the goal of minimization of the balancing cost.
Unforeseeable accepted and rejected divisible bids
If a set of optimal solutions exists, which lead however to different marginal prices: preference - smaller marginal price - because of transparency
The majority of BSPs agrees with the minimization of the cross-border flows.
Two optimal solutions with different marginal prices

## Slide 18
Feedback from the Consultation
SETTLEMENT

## Slide 19
Feedback Settlement – Main Input
Request for further analysis on the effects of XBMP on imbalance pricing.
Stakeholders do not see additional negative impacts of XBMP.
Cross-border marginal pricing
Stakeholders are in favor of block settlement. However, it has been argued, that the relation to TSO-BRP (imbalance adjustment) remains unclear.
Volume Settlement
Stakeholders prefer pricing category A (Main argument: most transparent).
Stakeholders prefer pricing option “A3” (Main argument: most transparent option). – ie. Same settlement price for direct and schedule activations. (Max. price of activated SA- and DA-bids of the main QH)
Majority of respondents are of the opinion that the greatest incentive to submit bids capable of direct activation can be achieved with pricing options “A3”.
Pricing Settlement

## Slide 20
Feedback Settlement – Main Input
About 50% of respondents consider the issue of “Rejected Scheduled bids/demand”* problematic, 50% do not.
No reasons were provided. Some of the stakeholders might have confused this issue with “Unforeseeably Rejected Divisible Bids (URB)”)
Rejected scheduled bids/demand
Wide consensus on how to treat price indeterminacies.
 Option1: “Mid point of marginal prices”. (Main reason: consistency with current practice in DA-market and foreseen practice in TERRE).
Price indeterminacies

## Slide 21
Feedback from the Consultation
CONGESTION MANAGEMENT
HARMONIZATION

## Slide 22
Feedback Congestion Management - Main Input
Overall, many inputs supported earlier proposal to SC as do not support measure mFRR zones, do not support measure to form a cluster, support measure Critical Network Elements in the future.
Limiting ATC - pushing internal congestions to borders by limiting ATC should not be allowed
Congestion Management

## Slide 23
Feedback Harmonization - Main Input
Harmonization of prequalification requirements:
Harmonization of accepted shape
Harmonization of mFRR GCT for BSPs
Harmonization of TSO-BSP settlement schemes
Harmonization of penalties scheme
Harmonization of back-up requirements (including energy availability requirements)
No specific feedback on preferences between before and after go-live harmonization
Harmonization Priorities

## Slide 24
Thank you for your attention!
For further details please contact:
Steering Committee Chairman
Martin Høgh Møller
mhm@energinet.dk
Technical Working Group Conveners
Aurelien Peyrac Markus Speckmann
aurelien.peyrac@rte-france.com Markus.speckmann@amprion.net